## Slide 1: Networking 8 Abril 2021

## Slide 2: Seguimos con direcciones IP. SUBNETTING
The IP address is comprised of the network ID and host ID fields, with a logically invisible separating line dividing the two.
This dividing line can be shifted, or “moved to the right,” by the network administrator to add configuration flexibility to the local-area network
Logical networks may be added to the configuration of the local infrastructure by reducing the amount of allowed hosts on the network
By subtracting available hosts, the amount of available networks or subnets is increased

## Slide 3: SUBNETTING; Dividing networks into smaller pieces called subnets
Split one large Network in smalller pieces
Minimizes Broadcast traffic
Keeps problems restricted to subnets
Isolating problems is important when things become big
When we have portions of network geographically separated

## Slide 4: SUBNETTING

## Slide 5: SUBNETTING
Individual departments may have different volume of traffic
If departments or subnets coexist in the same logical network they will compete for network bandwidth
Split problems into smaller pieces. This is also good for other questions in life…….
Bandwidth dedicated for every subnet. Collision traffic minimized
Different LAN protocol may coexist

## Slide 6: SUBNETTING and Network MASK
Mask used to reveal SUBNETS contained in the IP address
Every node in the same subnet must have the same Subnet MASK
Using SUBNET MASK routing devices may calculate which devices are on the same subnet
MASK: 32 bit binary numbering system
All subnets seems a unique net from outside the Network domain.

## Slide 7: Subnetting and MASK
Class A: 255.0.0.0
Class B: 255.255.0.0
Class C: 255.255.255.0
These are default Masks when no subnetting is performed.
Determining the number of networks and hosts you may calculate the right mask
The octet value 0 is reserved for the network segment address and NOT used for host addressing
The octet value 255 is reserved for broadcast message to all host in the subnet

## Slide 8: SUBNETTING
Network Address: 172.16.0.0
Subnet mask: 255.255.0.0
We “borrow” 255 units to extend network portion
11111111.11111111.00000000.00000000
11111111.11111111.11111111.00000000
We have created 8-bit subnet by changing the default mask
Subnet 172.16.1.0 has host range of: 172.16.1.0 to 172.16.1.254
172.16.1.255 reserved as BROADCAST address for that subnet

## Slide 9: CIDR: Calsses Interdomain Routing
Uses MASK to determine target network instead of classical “classful” addressing
In CIDR notation the IP address correspond to the network ID is called PREFIX

## Slide 10: CIDR Addressing: SLASH NOTATION

## Slide 11: IP address Class and Subnet MASK

## Slide 12: IP addressing and Subnet Mask

## Slide 13: IP Subnet Zero
IP SUBNET ZERO
204.1.1.0/24 prefix Length
255.255.255.0 represents
The entire network
204.1.1.0/28 (255.255.255.240)
Represents first subnet
Both uses the same IP address
But are handled different by
Routing protocols due to the
Four position bit jump and
Subnet mask assignment

## Slide 14: Host Address: Class C

## Slide 15: Subnet Table for Class C

## Slide 16: Class B Subnet Addressing

## Slide 17: Class B Subnet Host Addressing

## Slide 18: Class B subnet structure

## Slide 19: Class A Subnet Structure

## Slide 20: Class A Subnet and Host Addressing
SEMANA PROXIMA TODOS!!!!!!!!

## Slide 21: Importante para IPv6

## Slide 22: VLSM: Variable Length Subnet Mask
VLSM is an advanced form of SUBNETTING
Subnets of variable lengths coexist under one unique netowrk
Its usueful to match different interfaces requirements per subnet

## Slide 23: VLSM
VLSM allows CLASSLESS routing protocols: EIGRP (Enhanced Interior Gateway Protocol), OSPF (Open Shortest Path First), RIPv2 (Routing Information Protocol version 2) to function with VLSM
CLASSFUL protocols as RIP and IGRP do not work with VLSM
MUY IMPORTANTE: VLSM y CLASSLESS protocols…… ! Pagina explicandolo en detalle para la proxima semana

## Slide 24: VLSM
More complex but similar to CIDAR
Allows subnetting in subnets…… nesting as enough Host bits are available to steal from the network address block

## Slide 25: VLSM and IP optimization
Class C network address: 204.1.1.0/24
Divide this network in two /25 subnetworks stealing 1 bit from the first available host ID bit field
This gives us two subnets: 204.1.1.0/25 and another 204.1.1.128/25
204.1.1.0/25 is used for subnet 0 and the other will continue to be manipulated and divided in two new /26 subnets: 204.1.1.128/26 for subnet 1 and the other is used to create 2 new /27 subnets
Continue till tun out of host ID bits to steal….. END

## Slide 26: Optimizing IP with VLSM
VLSM subnet. Class C

## Slide 27: Summarization
Summarization is also named “route aggregation” or SUPERNETTING.
Is the consolidation of many individual routes into a single route
Is the reverse process of SUBNETTING
The supernet is a block of subnets addressed as a one complete network. Many network ID combined into one network address
Has minimum impact on routing procedures
By summarizing routes and having less routing tables entries, routers hardware gain in effficiency

## Slide 28: Summarizartion: Example
How routers view individual routes comparedwith route summarization
Four addressed summarized into 204.1.4.0/22

## Slide 29: Summarization: Example
Convert all addresses to binary format
Identify only the common bits from the four addresses ignoring all other bits
Convert this common bits back to decimal
We already have calculated our summarization routing address
By totalling those common bits it is easy to figure our your prefix length (subnet mask)

## Slide 30: Summarization and VLSM

## Slide 31: The ANDing Procedure

## Slide 32: TEST

## Slide 33: TEST

## Slide 34: SOLUCION
1-C. 254 (256-2) host addresses available
2-B. Creates sub-subnets of different lengths. VLSM allows creation of subnets of various lengths to better accommodate number of interfaces required per subnet
3-D. no ip subnet –zero
4-B. 3 bits; steal the first 3 host ID bits(from left to right) and convert to decimal (224) giving you the mask 255.255.224.0 or /19 in CIDR notation
5-A,B,C Route Aggregation, supernetting and summarization are used to refer consolidation of many individual routes
6- B,C,D. Separating Boradcast traffic, problem isolation and simplify management
7. B,D,E,F
8-B. 255.255.255.240, borrowing 4 hostbits from the fourth octet allows14host on 16 subnetted networks
9-C. 105.0.0.0 105.0.0.0/8 is the only valid class A address
10-A. Host IP204.201.210.4 is a class C host Address.

## Slide 35: ¡Muchas gracias!
Juan Ignacio Alonso Montull
Jignacio.alonso.montull@gmail.com