## Slide 1: Networking. Clase 7, 22 Abril 2021

## Slide 2: IPv6
IPv4: 32 bit addressing scheme, that allows roughly 4 billion Host on 16 million Networks
Considereing NAT (Network Address Translation) and Private addressing seems enough.
A,B, and C Classes have inflated the internetwork routing tables and proven to be WASTEFUL method of IP assignment
In mid 1990`s IPv6 was proposed to overcome IP inneficiencies (RFC 2460) by the IETF “Internet Engieneering Task Force”
Final standarisation of IPv6 in 1998
Version 5 was already assigned to another developing protocol, the Internet Stream Protocol. Thats os why we go from IPv4 to v6

## Slide 3: IPv6
Both Versions are similar in the way they work, they use different types of packet header formatting and addressing lengths
Ipv6 Packet Header is more efficient and greatly simplified. This helps to reduce processing overhead

## Slide 4: IPv6
IPv6 is a 128 bit address scheme. That means greater address space
IPv4 can function on IPv6. That has been a design premise.
IPv6 is supported by CISCO from IOS release 12.2 and later
IPv6 support STATELESS AUTOCONFIGURATION: a feature used to issue and generate IP address without the need of a DHCP (Dynamic Host Configuration Protocol) Server
    Routers send RZ (router advertisement) to Network Host containing the first half of the address (64 bit)
    The second half is generated by the host and it is known as INTERFACE IDENTIFIER, that uses its own MAC address or a random generated number. This allows the host to keep hardware addresses hidden for security reasons

## Slide 5: IPV6
Efficient Packets Headers. Fewer header fields must be read by routers and header checksums are completely discarded in IPv6. save router resources and improve network performance
Changes in Multicast Operations. Multicasting in IPv6 is mandatory instead of optional. This completely replace the broadcasting functionality in Ipv4
IPv6 replaces BROADCASTING with an “ALL HOST” multicasting group
Increased Security. IPsec is MANDATORY and natively implemented in IPv6
Additional Mobility features. A mobile Ipv6 node may change links and locations and keep one permanent address
Integrated Quality of Service QoS. Routers may organize , priorize and forward packets more efficiently and critical services SLA may be assured

## Slide 6: IPv6
128 bit- HEXADECIMAL addressing method called COLON EXADECIMAL NOTATION. 3,4 x 10^38 direcciones
Cada habitante de la tierra puede tener 5x 10^28 direcciones !!!!! Se termina con la escasez de direcciones de una vez. Once for all!!!
Subnet MASK are no longer used in IPv6, although SuBNETS are still determined by prefix length notation
IPv6 are 8 sets of 16 bit groups separated by colons

## Slide 7: IPv6
Splitting the 16 bit address into 8 bit
2FEE: 2F in binary is: 00101111 and EE??

## Slide 8: IPv6 Address Space

## Slide 9: IPv6 Who´s in charge
Who’s the assigning authority?
IPv6 address assignment is handled similarly to IPv4 address allocation.
Management of IPv6 addresses has been delegated from the Internet
Corporation Assigned Names and Numbers (ICANN) to the Internet Assigned
Numbers Authority (IANA), which in turn has been handed over to five
regional Internet registries (RIRs):
✦ The American Registry for Internet Numbers (ARIN): Serving North
America
✦ The Réseaux IP Européens Network Coordination Centre (RIPE NCC):
Supporting Europe, the Middle East, and the former Soviet Union
✦ The Asian Pacific Network Information Centre (APNIC): Supporting
Asia and Australia
✦ The African Network Information Centre (AfriNIC): Responsible for
Africa and the Indian Ocean
✦ The Latin American and Caribbean Internet Addresses Registry
(LACNIC): Serving Latin America and the Caribbean
These five RIRs delegate addressing responsibilities further to
✦ Local Internet registries (LIRs)
✦ Internet service providers (ISPs)

## Slide 10: IPV6 Address Notation
IPv6 128-bit addresses consist of two logical parts:
✦ The top 64 bits represent the global routing prefix (plus the subnet ID).
✦ The remaining 64 bits contain the host interface identifier.
The ultimate deciding factor of where the network portion ends and the host
portion starts remains the responsibility of the prefix length value (much
like IPv4 CIDR notation). This network/host split is not hard-coded into the
address and can be configured according to network requirements.
The host address functions the same way as the 48-bit hexadecimal MAC
address in IPv4, but has now added 16 additional bits.
The host address in IPv6 is created using the hardware MAC address from the host interface and is termed a 64-bit Extended Unique Identifier (EUI-64).
If privacy is a concern, the host can use a randomly generated number instead of the MAC address to identify itself on the network.

## Slide 11: Ipv6 Address Notation

## Slide 12: IPv6 Address Notation

## Slide 13: Ipv6 Address Notation

## Slide 14: IPv6 Address Types
Unicast. Packet Delivery for HOST to Host Communication. One unicast address is assigned per interface
Multicast: Addresses that are assigned to a specific “multicast group” of interfaces. IPv6 multicasting functions similarly to IPv4 broadcasting and
is described as “one-to-many” IP communications. Because no broadcast
address exists in IPv6,.
Compared to IPv4 broadcasting, IPv6 multicasting provides a much
more efficient means of group communications. It is no longer necessary
for all interfaces on the subnet to receive the same broadcast message,
saving valuable CPU processes and reducing network traffic.
Any cast: Packets that are sent and received by only one member
(interface) per any cast group. This is described as “one-to-one-of-many”
communications and delivers packets to the closest interface (in routing
distance) in the anycast group. Anycast addresses use the same syntax
as unicast addressing, and hosts are unable recognize the difference
between unicast and anycast packets.
There is an important difference to remember regarding any cast and
multicast delivery. Any cast packets are only sent to one host in an
Any cast group, compared to packets reaching “all hosts” in the multicast
group.

## Slide 15: IPV6 Reserved Address
:: — The unspecified address: Consists of all 0s and is sent by hosts that
do not know its own address. A network device sending a DHCP request
would be an example of using the unspecified address. The unspecified
address is 0:0:0:0:0:0:0:0, or written as two double colons.
::1 — The loopback address: As in IPv4, the loopback address is used for testing stack operability on a single interface, and packets are
looped back, or returned, to the same sending device. Packets are not
transmitted to remote machines. The loopback address is 0:0:0:0:0:0:0:1,
or written as two double colons followed by the number 1.
FE80::/10 — Link-local addresses: The first group of bits starting with FE in hex represent private addresses. These addresses are used much like the private addresses in IPv4 and cannot be routed. Packets that are sent to these private addresses stay on the local network and do not traverse routers to outside organizations. This is analogous to the IPv4
autoconfiguration addresses 169.254.0.0/16.
FF00::/8 Multicast Address. The first froup of bits FF (1111 1111) for dedicated multitask addressing

## Slide 16: IPv6 Adresses

## Slide 17: IPv6 Address Autoconfiguration
Address autoconfiguration allows IPv6 hosts to self-configure themselves with IP addressing and other information without the need for a server.
In IPv4,you either specify a static IP address or enable DHCP addressing to providerequired stateful information to hosts. Stateful addressing is delivered to clients using a centrally managed server. With stateless IPv6 autoconfiguration, neither a DHCP server nor static IP is necessary.
Stateless configuration allows devices to generate their own addresses and adjust according to the state of the network

## Slide 18: IPv6 Autonfiguration.
1. Generate a link-local address: The device creates a 64-bit host identifier using its own 48-bit hardware address and adds a trailing 16-bit hex value of 0xFFFE.
The 48-bit hardware address and the added 16-bit value of 0xFFFE combine to form the host identifier. The universal/local bit of
the MAC address is always the seventh bit and gets “flipped” from 0 to 1.
This process is called MAC-to-EUI64 conversion and determines the
interface ID of the device.
Another method can be used to generate the link-local address without
using a MAC address. Instead of using the hardware address of an
interface, a random “token” value is generated by the device. This can cause problems if two devices on the network randomly generate the
same token. The chances are minimal, but testing must be done to
eliminate the possibility that this token value is identically generated
and used somewhere else on the same local network.

## Slide 19: IPv6. Autoconfiguration.
2. Test the uniqueness of the link-local address: The host sends a neighbor solicitation message by employing the Neighbor Discovery Protocol (NDP).
NDP verifies the uniqueness of the link-local address. Because two nodes
may not share the same interface ID, the node listens on the network for
a neighbor advertisement. If duplicate addresses exist (most likely from
using a “token” value instead of the MAC address), a new interface ID
must be generated.
3. Assign the link-local address to the interface: The device assigns the newly generated link-local address to its interface. Assigning the link local address depends on the previous step and will execute only when
the address uniqueness test passes.

## Slide 20: IPv6. Autoconfiguration.
4. Host contacts the router on the local network: The host contacts
the router in one of two ways.
The host may either listen to router advertisements (RAs) or send its own router solicitation message. In either case, the requesting node contacts the router, requesting additional information needed for network address configuration.
The router responds and informs the host how to determine its globally unique network address. For networks employing stateful configurations,DHCPv6 contact information is provided to the host.
5. Globally unique network address is formed: The host combines the interface ID with the router-issued network prefix to create the globally
unique network address
While stateless address autoconfiguration has removed the major reasons for deploying DHCP services in IPv4, DHCPv6 may still be used in IPv6 networks to provide stateful addressing assignment.

## Slide 21: IPv6 Dynamic Approach

## Slide 22: IpV6 DHCP differences

## Slide 23: CISCO Example

## Slide 24: ICMPv6
Internet Control Message Protocol version 6 (ICMPv6) is an integral part
of IPv6 and functions just as it does in IPv4. ICMPv6 is used by nodes for
reliability testing (using the ping command) and for reporting errors during
packet handling. ICMPv6 messages are divided into two categories: error
messages and informational messages. These are defined by their high order bits in the message type field of each packet:
✦ 0–127 is the range for error messages.
✦ 128–255 are used for informational messages.
ICMPv6 packets are used for path MTU discovery, Neighbor Discovery Protocol (NDP), and the Multicast Listener Discovery (MLD) Protocol.
MLD is tasked with discovering nodes that want to send/receive multicast
packets to specific multicast addresses using IPv6 routers. Neighbor
Discovery uses ICMP messages to determine link-layer addresses of hosts that reside on the same network using solicitation messages.
Router advertisement (RA) messages are also handled by ICMPv6.

## Slide 25: IPv6 ROUTING
The Internet is a collection of IP-based packet-switching networks known
individually as autonomous systems (ASs). Each of these subnets may use one or more system administrators to deploy routing protocols inside the organization, known as Interior Gateway Protocols (IGPs).
To connect individual networks and to pass routing information between them, an Exterior Gateway Protocol (EGP) is enabled.
System administrators may either
✦ Manually update routing tables, which is called static routing
✦ Use an automatically configured dynamic routing approach
The purpose and goal of routing IPv4 and IPv6 packets remain the same: to forward packets efficiently from sender to receiver interfaces.

## Slide 26: IPv6 Routing
Static routing is implemented essentially the same way as in IPv4. Static
routes are configured and stored in static routing tables and maintained on the router itself. This may improve routing performance but also increases network management and administrative tasks.
Routers using an IPv6 static configuration have the following benefits over dynamically configured networks:
✦ Less bandwidth requirements
✦ Security and resource efficiency
✦ No CPU usage during route calculations
The drawbacks are that static routes must be manually reconfigured by
the network administrator if the network topology undergoes any changes.
Static routes can provide increased security for certain links on large networks or are optimally used for small networks with only one connection to the outside world.

## Slide 27: IPv6 Routing Protocols
IPv6 relies on the same routing protocols as does IPv4, although some
modifications and upgrades were made to provide the additional requirements of IPv6.
I examine three of the most popular Interior Gateway Protocols
modified for IP version 6:
✦ RIPng (RIP next generation)
✦ EIGRPv6
✦ OSPFv3
NEXT CLASS ALLOF YOU WILL PRESENT a 2 SLIDE WORK presenting those protocols in IPV6 and differences with IPV4

## Slide 28: IPv6 MIGRATION
✦ Develop a plan. Start working on a plan now before it is time to migrate. A complete transition to IPv6 can take years, so start planning thoroughly now. Address assignment, routing, DNS, and application support are areas that must be considered for deployment.
✦ Analyze the organization’s network management system. The majority of network management systems currently support IPv4 only. Additional funds may be required to upgrade the existing IPv4 network management system to IPv6, or an entirely new system may be needed to support IPv6.
✦ Evaluate network security. Unauthorized network access is still a major concern with IPv6. Both firewalls and intrusion detection systems are invaluable.
✦ Enable IPv6 on the network. Start activating IPv6 on the network core, or backbone, to the desktop. Applications may then follow suit and be migrated individually, depending on greatest organizational priority.

## Slide 29: IPv6 MIGRATION
To successfully migrate to IPv6, you must maintain backward compatibility with current IPv4 hosts and networks.
The IETF has recommended migration methods to follow that can ease the Internet conversion process to IPv6. A few methods I focus on are as follows:
✦ Dual-stack — IPv4 and IPv6 protocol stacks
✦ Tunneling — IPv6 through IPv4 and vice versa
✦ Translating addresses using NAT-PT

## Slide 30: Ipv6 Migration. DUAL STACK
Dual-stack environments allow functionally of both IPv4/IPv6 protocols
and applications to coexist on the same network.
This approach splits the traffic into two separate networks, so separate security strategies are also required:
Using IPv4 addresses in the dual stack-approach. The Ipv4 stack is used. Likewise for IPv6 addresses, the IPv6 stack is also used
If destination address is a IPV6 address with an embebed IPv4 address, IPv6 to IPv4 encapsulation is performed
In a network coexist both addressing. IPv6 Hjost send messages to IPv6 destiny, and the same for IPv4. Two logical networks on the same physical layer.

## Slide 31: IPv6 Migration. Tunneling
Each Tunnel is considered a Point to Point Link
Tunneling end points requires support for both IPv6 and IPv4 stacks

## Slide 32: IPv6 Tunneling. CISCO case

## Slide 34: IPv6 Migration. Tunneling

## Slide 35: IPv6 Migration. NAT-Protocol Translation
NAT-PT provides Bidirectional Address translation between IPv6 and IPv4 Hosts or domains and is designed to alleviate burdens for organizations transitioning from IPv4 to IPv6
Te translation service acts as a buffer and allows IPv4 hosts to communicate directly with IPv6 hosts and vice versa.
Dual Stack Networks with minimal IPv6 hosts may enable NAT-PT on routers to communicate with IPv4 only networks and hosts
GREAT ADVANTAGE: all configuration is performed at router level with no changes needed at the host. This allows IPV6 implementation with no disruption on network architecture.
NAT-PT NOT SHOULD BE USED when connectivity is needed between a dual stack IPv6/IPv4 host and a IPV4 only or IPV6 only hosts.
CISCO recommend tunneling over NAT-PT to eliminate the possibility of double translation

## Slide 36: IPv6 Migration NAT-PT
NAT-PT uses Stateless IP/ICMP Translation (SIIT) Algorithm and acts as a dedicate device tor translate between IPv6 and IPv4
NAT-PT activate a pool of IPv4 addresses and assigns them dynamically to IPv6 Nodes.

## Slide 37: NAT-PT example on CISCO Routers.

## Slide 38: HOMEWORK

## Slide 39: HOMEWORK

## Slide 40: ¡Muchas gracias!
jignacio.alonso.montull@gmail.com