## Slide 1
Serial Peripheral Interface
Dan Le
Niranjan Ramadas
Michael Starch
Stepan Tikhonov

## Slide 2
Introduction
What is it?
Basic Serial Peripheral Interface (SPI)‏
Capabilities
Protocol
Pro / Cons and Competitor
Uses
Conclusion
Serial Peripheral Interface
http://upload.wikimedia.org/wikipedia/commons/thumb/e/ed/
SPI_single_slave.svg/350px-SPI_single_slave.svg.png

## Slide 3: What is SPI?
Serial Bus protocol
Fast, Easy to use, Simple
Everyone supports it

## Slide 4
SPI Basics
A communication protocol using 4 wires
  Also known as a 4 wire bus
Used to communicate across small distances
Multiple Slaves, Single Master
Synchronized

## Slide 5
Capabilities of SPI
Always Full Duplex
  Communicating in two directions at the same time
  Transmission need not be meaningful
Multiple Mbps transmission speed
Transfers data in 4 to 16 bit characters
Multiple slaves
  Daisy-chaining possible

## Slide 6
Protocol
Wires:
  Master Out Slave In (MOSI)‏
  Master In Slave Out (MISO)‏
  System Clock (SCLK)‏
  Slave Select 1…N
Master Set Slave Select low
Master Generates Clock
Shift registers shift in and out data

## Slide 7
Wires in Detail
MOSI – Carries data out of Master to Slave
MISO – Carries data from Slave to Master
  Both signals happen for every transmission
SS_BAR – Unique line to select a slave
SCLK – Master produced clock to synchronize data transfer

## Slide 8
Shifting Protocol
Master shifts out data to Slave, and shift in data from Slave
http://upload.wikimedia.org/wikipedia/commons/thumb/b/bb/SPI_8-bit_circular_transfer.svg/400px-SPI_8-bit_circular_transfer.svg.png

## Slide 9
Diagram
Master and multiple independent slaves
http://upload.wikimedia.org/wikipedia/commons/thumb/f/fc/SPI_three_slaves.svg/350px-SPI_three_slaves.svg.png
Master and multiple daisy-chained slaves
http://www.maxim-ic.com/appnotes.cfm/an_pk/3947
Some wires have been renamed

## Slide 10
Clock Phase (Advanced)‏
Two phases and two polarities of clock
Four modes
Master and selected slave must be in same mode
Master must change polarity and phase to communicate with slaves of different numbers

## Slide 11
Timing Diagram
Timing Diagram – Showing Clock polarities and phases
http://www.maxim-ic.com.cn/images/appnotes/3078/3078Fig02.gif

## Slide 12
Pros and Cons
Pros:
Fast and easy
  Fast for point-to-point connections
  Easily allows streaming/Constant data inflow
  No addressing/Simple to implement
Everyone supports it
Cons:
SS makes multiple slaves very complicated
No acknowledgement ability
No inherent arbitration
No flow control

## Slide 13
Uses
Some Serial Encoders/Decoders, Converters, Serial LCDs, Sensors, etc.
Pre-SPI serial devices
PPC
  PPC implements SPI well
  The bus of choice for communicating with small peripherals

## Slide 14
Conclusion
SPI – 4 wire serial bus protocol
  MOSI MISO SS SCLK wires
Full duplex
Multiple slaves, One master
Best for point-to-point streaming data
Easily Supported

## Slide 15
Questions
Further information and sources:
Designing Embedded Hardware by John Catsoulis
“Introduction to Serial Peripheral Interface” by David Kalinsky and Roee Kalinsky (Embedded.com)
Programming Embedded Systems by Michael Barr and Anthony Massa
“SPI - Serial Peripheral Interface” at http://www.mct.net/faq/spi.html
Wikipedia.org – Serial Peripheral Interface Bus