## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 7
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 7 :: Topics
Introduction
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor
Exceptions
Advanced Microarchitecture

## Slide 3
Microarchitecture: how to implement an architecture in hardware
Processor:
  Datapath: functional blocks
  Control: control signals
Introduction

## Slide 4
Multiple implementations for a single architecture:
  Single-cycle: Each instruction executes in a single cycle
  Multicycle: Each instruction is broken into series of shorter steps
  Pipelined: Each instruction broken up into series of steps & multiple instructions execute at once
Microarchitecture

## Slide 5
Program execution time
Execution Time = (#instructions)(cycles/instruction)(seconds/cycle)
Definitions:
  CPI: Cycles/instruction
  clock period: seconds/cycle
  IPC: instructions/cycle = IPC
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance
Processor Performance

## Slide 6
Consider subset of MIPS instructions:
  R-type instructions: and, or, add, sub, slt
  Memory instructions: lw, sw
  Branch instructions: beq
MIPS Processor

## Slide 7
Determines everything about a processor:
  PC
  32 registers
  Memory
Architectural State

## Slide 8
MIPS State Elements

## Slide 9
Datapath
Control
Single-Cycle MIPS Processor

## Slide 10
STEP 1: Fetch instruction
Single-Cycle Datapath: lw fetch

## Slide 11
STEP 2: Read source operands from RF
Single-Cycle Datapath: lw Register Read

## Slide 12
STEP 3: Sign-extend the immediate
Single-Cycle Datapath: lw Immediate

## Slide 13
STEP 4: Compute the memory address
Single-Cycle Datapath: lw address

## Slide 14
STEP 5: Read data from memory and write it back to register file
Single-Cycle Datapath: lw Memory Read

## Slide 15
STEP 6: Determine address of next instruction
Single-Cycle Datapath: lw PC Increment

## Slide 16
Write data in rt to memory
Single-Cycle Datapath: sw

## Slide 17
Read from rs and rt
Write ALUResult to register file
Write to rd (instead of rt)
Single-Cycle Datapath: R-Type

## Slide 18
Determine whether values in rs and rt are equal
Calculate branch target address:
BTA = (sign-extended immediate << 2) + (PC+4)
Single-Cycle Datapath: beq

## Slide 19
Single-Cycle Processor

## Slide 20
Single-Cycle Control

## Slide 21
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
Review: ALU

## Slide 22
Review: ALU

## Slide 23
ALUOp1:0 | Meaning
00 | Add
01 | Subtract
10 | Look at Funct
11 | Not Used
ALUOp1:0 | Funct | ALUControl2:0
00 | X | 010 (Add)
X1 | X | 110 (Subtract)
1X | 100000 (add) | 010 (Add)
1X | 100010 (sub) | 110 (Subtract)
1X | 100100 (and) | 000 (And)
1X | 100101 (or) | 001 (Or)
1X | 101010 (slt) | 111 (SLT)
Control Unit: ALU Decoder

## Slide 24
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 |  |  |  |  |  |  | 
lw | 100011 |  |  |  |  |  |  | 
sw | 101011 |  |  |  |  |  |  | 
beq | 000100 |  |  |  |  |  |  | 
Control Unit Main Decoder

## Slide 25
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 0 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
Control Unit: Main Decoder

## Slide 26
Single-Cycle Datapath: or

## Slide 27
No change to datapath
Extended Functionality: addi

## Slide 28
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 |  |  |  |  |  |  | 
Control Unit: addi

## Slide 29
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 | 1 | 0 | 1 | 0 | 0 | 0 | 00
Control Unit: addi

## Slide 30
Extended Functionality: j

## Slide 31
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000010 |  |  |  |  |  |  |  | 
Control Unit: Main Decoder

## Slide 32
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000010 | 0 | X | X | X | 0 | X | XX | 1
Control Unit: Main Decoder

## Slide 33
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC
Review: Processor Performance

## Slide 34
Single-cycle:
  + simple
  cycle time limited by longest instruction (lw)
  2 adders/ALUs & 2 memories
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times
Same design steps: datapath & control
Multicycle MIPS Processor

## Slide 35
Replace Instruction and Data memories with a single unified memory – more realistic
Multicycle State Elements

## Slide 36
STEP 1: Fetch instruction
Multicycle Datapath: Instruction Fetch

## Slide 37
Multicycle Datapath: lw Register Read
STEP 2a: Read source operands from RF

## Slide 38
Multicycle Datapath: lw Immediate
STEP 2b: Sign-extend the immediate

## Slide 39
Multicycle Datapath: lw Address
STEP 3: Compute the memory address

## Slide 40
Multicycle Datapath: lw Memory Read
STEP 4: Read data from memory

## Slide 41
Multicycle Datapath: lw Write Register
STEP 5: Write data back to register file

## Slide 42
Multicycle Datapath: Increment PC
STEP 6: Increment PC

## Slide 43
Write data in rt to memory
Multicycle Datapath: sw

## Slide 44
Read from rs and rt
Write ALUResult to register file
Write to rd (instead of rt)
Multicycle Datapath: R-Type

## Slide 45
rs == rt?
BTA = (sign-extended immediate << 2) + (PC+4)
Multicycle Datapath: beq

## Slide 46
Multicycle Processor

## Slide 47
Multicycle Control

## Slide 48
Main Controller FSM: Fetch

## Slide 49
Main Controller FSM: Fetch

## Slide 50
Main Controller FSM: Decode

## Slide 51
Main Controller FSM: Address

## Slide 52
Main Controller FSM: Address

## Slide 53
Main Controller FSM: lw

## Slide 54
Main Controller FSM: sw

## Slide 55
Main Controller FSM: R-Type

## Slide 56
Main Controller FSM: beq

## Slide 57
Multicycle Controller FSM

## Slide 58
Extended Functionality: addi

## Slide 59
Main Controller FSM: addi

## Slide 60
Extended Functionality: j

## Slide 61
Main Controller FSM: j

## Slide 62
Main Controller FSM: j

## Slide 63
Review: Single-Cycle Processor

## Slide 64
Review: Multicycle Processor

## Slide 65
Temporal parallelism
Divide single-cycle processor into 5 stages:
  Fetch
  Decode
  Execute
  Memory
  Writeback
Add pipeline registers between stages
Pipelined MIPS Processor

## Slide 66
Single-Cycle vs. Pipelined

## Slide 67
Pipelined Processor Abstraction

## Slide 68
Single-Cycle & Pipelined Datapath

## Slide 69
WriteReg must arrive at same time as Result
Corrected Pipelined Datapath

## Slide 70
Same control unit as single-cycle processor
Control delayed to proper pipeline stage
Pipelined Processor Control

## Slide 71
When an instruction depends on result from instruction that hasn’t completed
Types:
  Data hazard: register value not yet written back to register file
  Control hazard: next instruction not decided yet (caused by branches)
Pipeline Hazards

## Slide 72
Data Hazard

## Slide 73
Insert nops in code at compile time
Rearrange code at compile time
Forward data at run time
Stall the processor at run time
Handling Data Hazards

## Slide 74
Insert enough nops for result to be ready
Or move independent useful instructions forward
Compile-Time Hazard Elimination

## Slide 75
Data Forwarding

## Slide 76
Data Forwarding

## Slide 77
Forward to Execute stage from either:
  Memory stage or
  Writeback stage
Forwarding logic for ForwardAE:
if ((rsE != 0) AND (rsE == WriteRegM) AND RegWriteM)
then ForwardAE = 10
else if ((rsE != 0) AND (rsE == WriteRegW) AND RegWriteW)
then ForwardAE = 01
else ForwardAE = 00
Forwarding logic for ForwardBE same, but replace rsE with rtE
Data Forwarding

## Slide 78
Stalling

## Slide 79
Stalling

## Slide 80
Stalling Hardware

## Slide 81
lwstall =
((rsD==rtE) OR (rtD==rtE)) AND MemtoRegE
StallF = StallD = FlushE = lwstall
Stalling Logic

## Slide 82
beq:
  branch not determined until 4th stage of pipeline
  Instructions after branch fetched before branch occurs
  These instructions must be flushed if branch happens
Branch misprediction penalty
  number of instruction flushed when branch is taken
  May be reduced by determining branch earlier
Control Hazards

## Slide 83
Control Hazards: Original Pipeline

## Slide 84
Control Hazards

## Slide 85
Introduced another data hazard in Decode stage
Early Branch Resolution

## Slide 86
Early Branch Resolution

## Slide 87
Handling Data & Control Hazards

## Slide 88
Forwarding logic:
ForwardAD = (rsD !=0) AND (rsD == WriteRegM) AND RegWriteM
ForwardBD = (rtD !=0) AND (rtD == WriteRegM) AND RegWriteM
Stalling logic:
branchstall = BranchD AND
[RegWriteE AND ((WriteRegE == rsD) OR (WriteRegE == rtD))
OR
[MemtoRegM AND ((WriteRegM == rsD) OR (WriteRegM == rtD))]
StallF = StallD = FlushE = lwstall OR branchstall
Control Forwarding & Stalling Logic

## Slide 89: Multicycle operations

## Slide 90: 1. Introduction
Pipelined processor
  All instruction have the same duration
  Ideal performance: CPI=1
  WAW and WAR hazards are avoided
  RAW hazards are avoided using forwarding
  RAW hazards in load instructions generate pipeline stalls. The compiler can help by scheduling the instructions.
  Control hazards. Stalls and forwarding.
  Instructions start and finish in order

## Slide 91: 2. Multicycle operations
¿ What happens if instructions have a different length?
  This happens when instructions require more than 1 cycle to execute
    Floating point operations
    Integer multiplication and division
Latency of a Functional Unit: Number of cycles to execute an instruction
Notes: Características de las Unidades funcionales (UF)
  Latencia de uso: número de ciclos de espera entre una instrucción que produce un resultado y una instrucción que lo usa. Suele ser un ciclo menos que la longitud del pipeline de ejecución ?????
  Intervalo de iniciación: Nº de ciclos que tiene que esperar otra instrucción para poder utilizar la unidad (en el caso de unidades segmentadas)

## Slide 92: 2. Multicycle operations
Problems
  Structural hazards
  Higher penalization of RAW hazards
  New WAW and WAR hazards
  Problems if out of order commit

## Slide 93: 3. Multicycle operations: structural haz
Structural hazard: Two instructions needing the same Functional Unit
  The second instruction must wait for the first instruction to finish its execution
Ciclo12
Clock
ADDD F3, F4,F6
ADDD F10, F2, F8
IF
ID
Ciclo2
Ciclo4
Ciclo5
Ciclo6
Ciclo3
Ciclo1
IF
ID
Add1
Add2
Ciclo7
IDp
Ciclo8
Mem
Ciclo9
Mem
WB
WB
Add3
Ciclo10
Ciclo11
IDp
The FP Adder has a latency of 3 cycles
Add1
Add2
Add3
  IDP stall due to structural hazard: the adder is not available
IDp
2 cycles waiting

## Slide 94: 3. Multicycle operations: structural haz
Solution: Pipelining the FU with a latency > 1
  Division is not usually pipelined, so in that case hazards must still be detected

## Slide 95: 3. Multicycle operations: structural haz
Ciclo12
Clock
ADDD F3, F4,F6
ADDD F10, F2, F8
IF
ID
Ciclo2
Ciclo4
Ciclo5
Ciclo6
Ciclo3
Ciclo1
IF
ID
Add1
Add2
Ciclo7
Ciclo8
Mem
Ciclo9
Mem
WB
WB
Add3
Ciclo10
Ciclo11
Add1
Add2
Add3
No stall in 2nd instruction
The FP Adder has a latency of 3 cycles
Structural hazard: Two instructions needing the same Functional Unit
  The second instruction can start executing in the next cycle

## Slide 96: 3. Multicycle operations: structural haz
Clock
MULTD F0,F4,F6
ADDD F2, F10,F8
IF
ID
Mem
Ciclo2
Ciclo4
Ciclo5
Ciclo7
Ciclo3
Ciclo1
IF
Mem
WB
WB
ID
Mul1
Mul2
Mul3
Add1
Add2
Ciclo8
Structural hazard: Two instructions arrive to MEM Stage at the same time
  Problems both in MEM and WB Stages
IDP stall due to structural hazard: Two instructions in MEM stage
IDp
Ciclo6
Mul4
Add3

## Slide 97: 3. Multicycle operations: structural haz
Solution 1:
  Stop the second instruction in ID Stage
Clock
MULTD F0,F4,F6
ADDD F2, F10,F8
IF
ID
Mem
Ciclo2
Ciclo4
Ciclo5
Ciclo7
Ciclo3
Ciclo1
IF
Mem
WB
WB
ID
Mul1
Mul2
Mul3
Add1
Add3
Ciclo8
IDp
Ciclo9
Ciclo6
Mul4
Add2

## Slide 98: 3. Multicycle operations: structural haz
Solution 2:
  Stop the conflicting instructions at the end of the execution
    Arbitration required in some cases
Clock
MULTD F0,F4,F6
IF
ID
Mem
Ciclo2
Ciclo4
Ciclo5
Ciclo7
Ciclo3
Ciclo1
IF
Mem
WB
WB
ID
Mul1
Mul2
Mul3
Add1
Add3
Ciclo8
Ciclo9
ADDD F2, F10,F8
IDP pstall due to structural hazard: Two instructions in MEM stage
Addp
Ciclo6
Mul4
Addp
Add2

## Slide 99: 4. Multicycle operations: RAW hazards
RAW hazard: Data provided by A-L instruction
  Forwarding does not avoid stalls
Clock
MULTD F2, F4,F6
ADDD F10, F2, F8
IF
ID
Ciclo2
Ciclo4
Ciclo5
Ciclo6
Ciclo3
Ciclo1
IF
ID
Mul1
Mul2
Mul3
Add1
Add2
Ciclo7
IDp
Ciclo8
Mem
Ciclo9
Mem
WB
WB
Add3
Ciclo10
Ciclo11
Mul4
IDp
IDp
  IDP Stall due to RAW hazard
IDp
Stall: 3 cycles
Notes: La lógica del cortocircuito es más compleja
  Más instrucciones implicadas
  Muchos más comparadores
  Bloqueos más largos

## Slide 100: 4. Multicycle operations: RAW hazards
IDp
IDp
IFp
IFp
IDp
IFp
Clock
Multd F0,F4,F6
ADDD F2, F0, F8
IF
ID
Mul1
Mem
Ciclo2
Ciclo4
Ciclo5
Ciclo6
Ciclo3
Ciclo7
Ciclo8
Ciclo1
Ciclo9
Ciclo10
Ciclo11
WB
SD F2, 2(R3)
Mul2
Mul3
Mul4
IF
ID
Add1
Add2
Add3
Mem
WB
IF
ID
Ex
Mem
WB
Ciclo12
Ciclo13
LD F4, 0(R12)
IDp
IFp
IF
IDp
IDp
ID
Ex
Ciclo14
Mem
What happens in a RAW hazard where data is provided by a load
  The instruction depending on the load must stall
  Forwarding does not avoid stalls
WB
6 cycles of stall
  IDP Stall due to RAW hazard
  IFP Stall due to structural conflict
IFp
IDp

## Slide 101: 5. Multicycle operations: OoO commit
Instructions may finish in a different order to the one they were launched
Problems:
  Structural hazard: Simultaneous write to the Register File
  New WAW hazards
Clock
Multd F0,F4,F6
ADDD F2, F10,F8
IF
ID
Mul1
Mem
Ciclo2
Ciclo4
Ciclo5
Ciclo6
Ciclo3
Ciclo7
Ciclo8
Ciclo1
Ciclo9
Ciclo10
Ciclo11
WB
ADD R2,R3,R4
ADD,R5,R6,R7
Mul2
Mul3
Mul4
Mul5
Mul6
Mul7
IF
ID
Add1
Add2
Add3
Add4
Mem
WB
IF
ID
Ex
Mem
WB
IF
ID
Ex
Mem
WB

## Slide 102: 6. Multicycle operations: WAW hazards
How do we handle a WAW hazard
  When the program finishes, F2 contains the result of the addition and not the result from the load
  This is an unfrequent situation, since ADDD F2, F10,F8 is completely useless
Clock
Ciclo2
Ciclo4
Ciclo5
Ciclo6
Ciclo3
Ciclo7
Ciclo8
Ciclo1
WB
Ciclo9
Ciclo10
Ciclo11
ADDD F2, F10,F8
LD F2, 0(R2)
IF
ID
Add1
Add2
Add3
Add4
Mem
IF
ID
Ex
Mem
WB
Multd F0,F4,F6
IF
ID
Mul1
Mem
WB
Mul2
Mul3
Mul4
Mul5
Mul6
Mul7

## Slide 103: 6. Multicycle operations: WAW hazards
Solution 1
  Stop the instruction creating the hazard (the second one)
  The number of stall cycles depends on the length of the first instruction and the distance among the two
Clock
Ciclo2
Ciclo4
Ciclo5
Ciclo6
Ciclo3
Ciclo7
Ciclo8
Ciclo1
WB
Ciclo9
Ciclo10
Ciclo11
ADDD F2, F10,F8
LD F2, 0(R2)
IF
ID
Add1
Add2
Add3
Add4
Mem
IF
ID
Ex
Mem
WB
IDp
IDp
Multd F0,F4,F6
IF
ID
Mul1
Mem
WB
Mul2
Mul3
Mul4
Mul5
Mul6
Mul7
  IDP Stall due to WAW hazard
IDp
2 ciclos de espera

## Slide 104: 6. Multicycle operations: WAW hazards
Solution 2
  Avoid write of the first instruction
Clock
Ciclo2
Ciclo4
Ciclo5
Ciclo6
Ciclo3
Ciclo7
Ciclo8
Ciclo1
WB
Ciclo9
Ciclo10
Ciclo11
ADDD F2, F10,F8
LD F2, 0(R2)
IF
ID
Add1
Add2
Add3
Add4
Mem
IF
ID
Ex
Mem
WB
Multd F0,F4,F6
IF
ID
Mul1
Mem
WB
Mul2
Mul3
Mul4
Mul5
Mul6
Mul7

## Slide 105: 7. Multicycle operations: WAR hazards
These hazards do not exist due to the pipeline design
  Read: In Decode Stage
  Write: Last Stage
Clock
Ciclo2
Ciclo4
Ciclo5
Ciclo6
Ciclo3
Ciclo7
Ciclo8
Ciclo1
WB
Ciclo9
Ciclo10
Ciclo11
ADDD F2, F0,F8
…
IF
ID
Add1
Add2
Add3
Add4
Mem
Multd F0,F4,F6
IF
ID
Mul1
Mem
WB
Mul2
Mul3
Mul4
Mul5
Mul6
Mul7

## Slide 106: Advanced Microarchitecture

## Slide 107
Deep Pipelining
Branch Prediction
Superscalar Processors
Out of Order Processors
Register Renaming
SIMD
Multithreading
Multiprocessors
Advanced Microarchitecture

## Slide 108
10-20 stages typical
Number of stages limited by:
  Pipeline hazards
  Sequencing overhead
  Power
  Cost
Deep Pipelining

## Slide 109
Ideal pipelined processor: CPI = 1
Branch misprediction increases CPI
Static branch prediction:
  Check direction of branch (forward or backward)
  If backward, predict taken
  Else, predict not taken
Dynamic branch prediction:
  Keep history of last (several hundred) branches in branch target buffer, record:
    Branch destination
    Whether branch was taken
Branch Prediction

## Slide 110
add $s1, $0, $0 # sum = 0
add $s0, $0, $0 # i = 0
addi $t0, $0, 10 # $t0 = 10
for:
beq $s0, $t0, done # if i == 10, branch
add $s1, $s1, $s0 # sum = sum + i
addi $s0, $s0, 1 # increment i
j for
done:
Branch Prediction Example

## Slide 111
Remembers whether branch was taken the last time and does the same thing
Mispredicts first and last branch of loop
1-Bit Branch Predictor

## Slide 112
Only mispredicts last branch of loop
2-Bit Branch Predictor

## Slide 113
Multiple copies of datapath execute multiple instructions at once
Dependencies make it tricky to issue multiple instructions at once
Superscalar

## Slide 114
lw $t0, 40($s0)
add $t1, $s1, $s2
sub $t2, $s1, $s3 Ideal IPC: 2
and $t3, $s3, $s4 Actual IPC: 2
or $t4, $s1, $s5
sw $s5, 80($s0)
Superscalar Example

## Slide 115
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 6/5 = 1.2
or $t3, $s5, $s6
sw $s7, 80($t3)
Superscalar with Dependencies

## Slide 116
Looks ahead across multiple instructions
Issues as many instructions as possible at once
Issues instructions out of order (as long as no dependencies)
Dependencies:
  RAW (read after write): one instruction writes, later instruction reads a register
  WAR (write after read): one instruction reads, later instruction writes a register
  WAW (write after write): one instruction writes, later instruction writes a register
Out of Order Processor

## Slide 117
Instruction level parallelism (ILP): number of instruction that can be issued simultaneously (average < 3)
Scoreboard: table that keeps track of:
  Instructions waiting to issue
  Available functional units
  Dependencies
Out of Order Processor

## Slide 118
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 6/4 = 1.5
or $t3, $s5, $s6
sw $s7, 80($t3)
Out of Order Processor Example

## Slide 119
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 6/3 = 2
or $t3, $s5, $s6
sw $s7, 80($t3)
Register Renaming

## Slide 120
Single Instruction Multiple Data (SIMD)
  Single instruction acts on multiple pieces of data at once
  Common application: graphics
  Perform short arithmetic operations (also called packed arithmetic)
For example, add four 8-bit elements
SIMD

## Slide 121
Multithreading
  Wordprocessor: thread for typing, spell checking, printing
Multiprocessors
  Multiple processors (cores) on a single chip
Advanced Architecture Techniques

## Slide 122
Process: program running on a computer
  Multiple processes can run at once: e.g., surfing Web, playing music, writing a paper
Thread: part of a program
  Each process has multiple threads: e.g., a word processor may have threads for typing, spell checking, printing
Threading: Definitions

## Slide 123
One thread runs at once
When one thread stalls (for example, waiting for memory):
  Architectural state of that thread stored
  Architectural state of waiting thread loaded into processor and it runs
  Called context switching
Appears to user like all threads running simultaneously
Threads in Conventional Processor

## Slide 124
Multiple copies of architectural state
Multiple threads active at once:
  When one thread stalls, another runs immediately
  If one thread can’t keep all execution units busy, another thread can use them
Does not increase instruction-level parallelism (ILP) of single thread, but increases throughput
Intel calls this “hyperthreading”
Multithreading

## Slide 125
Multiple processors (cores) with a method of communication between them
Types:
  Homogeneous: multiple cores with shared memory
  Heterogeneous: separate cores for different tasks (for example, DSP and CPU in cell phone)
  Clusters: each core has own memory system
Multiprocessors

## Slide 126
Patterson & Hennessy’s: Computer Architecture: A Quantitative Approach
Conferences:
  www.cs.wisc.edu/~arch/www/
  ISCA (International Symposium on Computer Architecture)
  HPCA (International Symposium on High Performance Computer Architecture)
Other Resources